## Slide 1: Design and Verification of a Synchronous FIFO Memory in Verilog
Under the guidance of
Puneet Kumar Sir, Shelly Gupta Mam.
Presented by- Saurav Singh

## Slide 2: Objective of the Project

## Slide 3: OBJECTIVE
The objective of this project is to design, implement, and verify a parameterized synchronous FIFO (First-In-First-Out) memory module using Verilog HDL. The FIFO facilitates orderly data buffering between producer and consumer circuits in synchronous digital systems.
This project focuses on:
Creating a configurable FIFO with adjustable data width and depth.
Ensuring proper handling of corner cases such as overflow, underflow, and pointer wrap-around.
Writing a comprehensive testbench to validate functionality through various test cases including reset behavior, simultaneous read/write, and boundary conditions like full and empty states.

## Slide 4: Introduction

## Slide 5: What is FIFO and Why is it Needed?
Need for FIFO:
Data Rate Matching: It helps in bridging systems with different data processing rates.
Clock Domain Isolation: In asynchronous FIFOs, it allows safe data transfer between different clock domains.
Flow Control: Manages temporary storage and smoothens data flow between sender and receiver.
What is FIFO?
FIFO stands for First-In, First-Out. It is a memory buffer or queue where the data that is written first is read first. It is typically implemented using a circular buffer with separate read and write pointers.

## Slide 6: Architecture of Synchronous FIFO Memory
1. Memory Array
Acts as the data buffer.
Size: DEPTH x DATA_WIDTH (e.g., 16 x 8).
Stores data between write and read operations.
2. Control Pointers
Write Pointer (wptr): Points to the next memory location to write data. Increments on wr_en, wraps around on overflow.
Read Pointer (rptr): Points to the next memory location to read data. Increments on rd_en, wraps around on overflow.
3. Circular Buffer Logic
Both pointers operate in a circular fashion using modulo operation.
Prevents overflows and underflows by managing memory efficiently.

## Slide 7
4. Counter
Tracks the number of valid entries in the FIFO.
Increases on write, decreases on read.
Drives full and empty flags:
  full = (count == DEPTH)
  empty = (count == 0)
5. Control Signals
clk: Synchronizes all operations.
rst: Resets FIFO state (pointers, counter, output).
wr_en: Enables writing to FIFO.
rd_en: Enables reading from FIFO.
6. Data Interface
Input (din): Data written into the FIFO.
Output (dout): Data read out from the FIFO.

## Slide 8: Designing the Synchronous FIFO
Component | Function
Memory Array (memory[0:DEPTH-1]) | Holds the data entries temporarily
Write Pointer (wptr) | Points to the location where new data will be written
Read Pointer (rptr) | Points to the location from where data will be read
Counter (count) | Tracks the number of elements in the FIFO
Full/Empty Flags | Indicates FIFO status: whether it's full or empty
Control Signals (wr_en, rd_en) | Enable write and read operations

## Slide 9: Working Principle
1). Write Logic
If wr_en is HIGH and FIFO is not full, data is written at wptr.
wptr is then incremented (with wrap-around using modulo).
2). Read Logic
If rd_en is HIGH and FIFO is not empty, data is read from rptr.
rptr is then incremented (circular behavior).
3). Status Logic
full = (count == DEPTH)
empty = (count == 0)

## Slide 12: Testbench and Test Cases
Test Case ID | Description
TC_01 | Write operation - Check if FIFO becomes non-empty after writing
TC_02 | Read operation - Verify correct data is read
TC_03 | Full condition - Fill FIFO and check full flag
TC_04 | Empty condition - Read the only element and check empty flag
TC_05 | Single write/read - Basic data integrity check
TC_06 | Multiple writes - Fill FIFO completely
TC_07 | Multiple reads - Read back all values and verify sequence
TC_08 | Reset functionality - Confirm FIFO clears on reset
TC_09 | Overflow handling - Write after FIFO is full, ensure no write occurs
TC_10 | Underflow handling - Read from empty FIFO, ensure no invalid data
TC_11 | Wrap-around - Validate pointer wrapping using reads and writes
TC_12 | Simultaneous read/write - Test behavior with both operations active
Test Cases Included:

## Slide 13: RESULTS

## Slide 14: TC_01 – Write Operation Test
Write operation - Check if FIFO becomes non-empty after writing

## Slide 15: TC_02 – Read Operation Test
Read operation - Verify correct data is read

## Slide 16: TC_03 – Full Condition Test
Full condition - Fill FIFO and check full flag

## Slide 17: TC_04 – Empty Condition Test
Empty condition - Read the only element and check empty flag

## Slide 18: TC_05 – Single Write/Read Test
Single write/read - Basic data integrity check

## Slide 19: TC_06 – Multiple Writes Test
Multiple writes - Fill FIFO completely

## Slide 20: TC_07 – Multiple Reads Test
Multiple reads - Read back all values and verify sequence

## Slide 21: TC_08 – Reset Functionality Test
Reset functionality - Confirm FIFO clears on reset

## Slide 22: TC_09 – Overflow Handling
Overflow handling - Write after FIFO is full, ensure no write occurs

## Slide 23: TC_10 – Underflow Handling
Underflow handling - Read from empty FIFO, ensure no invalid data

## Slide 24: TC_11 – Wrap-Around Test
Wrap-around - Validate pointer wrapping using reads and writes

## Slide 25: TC_12 – Simultaneous Read/Write Test
Simultaneous read/write - Test behavior with both operations active

## Slide 26: Conclusion
1). Reliable Data Buffering The designed synchronous FIFO successfully enables temporary storage and transfer of data between producer and consumer modules, ensuring data integrity under a single clock domain.
2). Efficient Resource Management With circular pointer logic, status flags (full/empty), and parameterized depth/width, the FIFO design is both memory-efficient and scalable for various digital systems.
3). Verified Functionality Extensive testbench coverage through 12+ test cases (including corner cases like overflow, underflow, and wrap-around) validates the robustness and correctness of the FIFO implementation.

## Slide 27: Thank You